## Slide 1: Adhesives
Wood Manufacturing & Finishing
Questions & Answers

## Slide 2: Q & A on Adhesives
What is Dermatitis?
Dermatitis is an inflammation of the skin usually starting with irritation and redness.
What is Occupational Dermatitis?
Occupational Dermatitis is caused by contact of the skin with certain materials. The hands and arms are usually affected first.
How can we prevent Dermatitis?
Wear rubber gloves and or use barrier creams and general washing.

## Slide 3: Q & A on Adhesives
Name the three main types of adhesives.
Animal Glue: (animal bones & hide & fish offal )
Vegetable Glue: (dextrine, rye, soya bean flour & rubber latex)
Mineral Glue: (synethic resins, coal tar & crude oil)

## Slide 4: Q & A on Adhesives
Give 3 advantages and 3 disadvantages for Animal Glue:
Advantages of Animal Glue Strong, great for curved veneering. Veneer can be re-softened when set and repositioned. Glue can be reheated and reused again. Cheap.
Disadvantages of Animal Glue Has to heated before use and applied hot. Can be quite pungent. Short Pot life. Quite messy.

## Slide 5: Q & A on Adhesives
Give 3 advantages and 3 disadvantages for P.V.A.
Advantages of P.V.A. Glue
Strong, in veneering setting times can be speeded up with heat, use straight from bottle. Exterior grade is water resistant.
Disadvantages of P.V.A. Glue Some grades take up to 1hr to set. If not cleaned off properly orange staining can occur when applying polish or lacquer. Reacts with metal and tannic acid in certain timbers to give blue staining

## Slide 6
What are the glues below used for?
Phenol formaldehyde.
Used for making plywood and Laminated plastics.
Resorcinol formaldehyde.
Glue-lam beams found in leisure centres, shopping centres etc.
Epoxy resin.
Bonds non porous material such as glass, plastic & metal.
Q & A on Adhesives

## Slide 7
What is meant by gap filling glues? Give example.
Glues that expand or don’t break down in loose joints. Urea Formaldehyde.
What is meant by separate application glues?
These glues are used with a catalyst or hardener. Coat one side with glue one side with hardener.
What is meant by mixed application glues?
liquid or powder glue and hardeners are weighed and mixed prior to application.
Q & A on Adhesives

## Slide 8
What is Epoxy resin?
These glues are two liquids that have to be mixed together before use. Used for bonding metal, glass, plastic & wood.
What is Neoprene?
These are either synthetic or natural rubber latex glues in solvents and set by evaporation. Used for laying veneers on shaped rims, laying plastic laminates.
Q & A on Adhesives

## Slide 9: Q & A on Adhesives
Name 1 glue for each job below & give 1 reason for each choice.
A Teak Garden Table:
Exterior P.V.A.: The glue would need to be Waterproof.
Repairing the veneer on an antique bow front drawer.
Animal Glue: The existing veneer would have been stuck using animal glue and any repairs would need to use the same glue.
Repairing a badly fitting joint:
Gap-filling Glue: The glue needs to fill in the gaps without breaking down at a later stage.
Gluing up an occasional table:
P.V.A. (interior) glue. It’s quick and easy to use, fairly strong set.

## Slide 10: Q & A on Adhesives
Give 3 advantages and 3 disadvantages for Urea Formaldehyde:
Advantages of Urea Formaldehyde Strong, water resistant, setting times can be speeded up with heat, great for pattern veneering, when set it is heat resistant
Disadvantages of Urea Formaldehyde Expensive, has to be weighed and mixed, can cause allergic reactions i.e. dermatitis, short pot life, dulls tool edges, fairly short shelf life, open bag can become air set.

## Slide 11: Q & A on Adhesives
What temperature should adhesive be applied?
Room temperature of 18º, adhesion may be effected if glue is applied in cold or damp conditions.
What is chilling when referring to glue?
If open time of gluing is left too long or glue is applied in cold conditions a skin may form on the outer surface of the glue.
What is show through when referring to glue in veneering?
If too much glue is used excess may be forced up through the veneer’s surface.

## Slide 12: Q & A on Adhesives
Describe briefly how contact adhesive is used to stick plastic laminate to a chipboard top.
Apply contact adhesive to the chipboard allow 10mins until its tacky.
Apply contact adhesive to the laminate and to the chipboard and leave until both become tacky. Position laminate on chipboard then press firmly expelling all air. Leave until set then Trim.