## Slide 1
Furniture Joints

## Slide 2: Butt Joints
A butt joint is made when two pieces of wood are butted together and glued.

## Slide 3: Name These Edge Joints
a
b
c
d
Comb joint, Tongue & groove & Slotted joint screw joint.
Rubbed glue joint
Dowel joint
Biscuit joint
Loose tongue joint

## Slide 4: Name these joints
E

## Slide 5: Name these joints
E
Scarf Joints
A : Rubbed Glue Joint
B : Tongue & Groove Joint
C : Biscuit Joint
D : Loose Tongue
E : Dowel Joint

## Slide 6: Comb joint

## Slide 7: Having / Lap joints
Lap joints are created when two pieces of wood overlap one another at a right angle. Very simple form of jointing.
Can you name another type of having?

## Slide 8: Mortise & Tenon
The mortise and tenon joint is one of the strongest traditional furniture joints. Usually found on good quality furniture.
It was sometimes reinforced with wedges, pegs or keys.
Lots of variations of these joints based on material being jointed and function of joint.

## Slide 9: Name these joints
1
2
3
4
5
6
8
7
9

## Slide 10: Name these joints
1 Bridle joint
2 Barefaced M & T
3 Scribed M & T
4 Mitred M & T
5 High & Low Shoulder
M & T
6 Fox wedged M & T
8 Corner Mitred
Bridle joint
7 Haunched M & T
9 Twin Tenon

## Slide 11: Keyed Mortice and Tenon

## Slide 12: Craftsmanspace Free technical plans, books, patterns, software
http://www.craftsmanspace.com/knowledge/keyed-mortise-and-tenon-joint.html
How to mark out a Key

## Slide 13: Corner Mitre Joints
The mitre joint usually cut at 45 degrees, on the ends of two pieces of wood, used on frames.
Can you name this bottom joint
Mitred bridle joint

## Slide 14: Housing joints
Jointing across the width shelf to side.
Can you draw Rebate housing, Dovetail housing

## Slide 15: Dovetails
The dovetail joint is one of the most distinctive and best antique furniture joints used in furniture construction to join wood at a right angle.
Recognised by the angled pieces that replicate doves’ tails.
They form a strong interlock able joint with a large gluing area.
Used for joining carcass ends and for creating drawers.
Wide variations available, used as features on high class furniture.

## Slide 16: Carcase Joints
1
2
5
4
6
3

## Slide 17: Carcase Joints
1 Through Dovetail
2 Lapped Dovetail
5 Secret Mitre Dovetail
4 Double Lapped
Dovetail
6 Through Pinned
Joint
3 Finger Joint

## Slide 18: Rule Joint
Rule joint hinge. Image from
woodworkersjournal.com
This joint is used on drop leaf tables. The rule joint is jointed
together using a rule joint hinge. The hinge has one leaf
longer than the other why?

## Slide 19: Knuckle Joint
Traditional moveable joint used on drop leaf tables

## Slide 20: Trend 9/41 Knuckle Joint Cutter
Cutter should be used in router table

## Slide 21: Name these joints
5
1
2
3
4
6

## Slide 22: Name these joints
5 Tennoned &
mitred clamped
1 Rule joint
2 Projected wedged
mortise & tennon
3 Knuckle joint
4 Dovetail Key
6 Housing joint

## Slide 23: Name these joints
3
5
4
1
2
6

## Slide 24: Name these joints
3 Hammer Head
Tenon joint
5 Machine Dovetails
4 Dovetail Halving
1 Stopped Housing
2 Stopped Dovetail
Housing
6 Bridle Joint

## Slide 25: Modern Jointing

## Slide 26: Dowels
Dowels a fast way of jointing.
Holes need to be aligned accurately.
Different patterns that allow glue to spread.

## Slide 27: Biscuits
Biscuits a faster way of jointing, small allowance for accuracy.

## Slide 28: Domino
Cross between a dowel and a biscuit you get a domino tenon
Festool domino joiner

## Slide 29: Beadlock Pro
Alternative to the mortice and tenon something similar to using a false tennon.

## Slide 30: JessEm Slip slot mortise mill
http://www.youtube.com/watch?v=_VtVGnxlBrc
This is based on false tenons. It is a jig and custom made
drill bit that can be used in any handheld drill.