## Slide 1
Sample Questions on Surface Finishes

## Slide 2: Q 1.
Describe briefly how to apply French Polish to a Solid Table Top.
French polish : Mix together shellac and methylated spirit. The polish is worked in slowly using a Fad, gradually building up a film of polish each coat is left to dry before applying the next coat. Each coat will partially dissolve the coat beneath so the layers will amalgamate.
J.Byrne 2016

## Slide 3: Q 2.
Describe briefly how to apply Oil to a Solid Table Top.
Oil : This is applied in numerous layers, each coat must be hardened by oxidization and at least 12 coats are needed. The addition of small amounts of turpentine make it easier for working and will speed up drying process each layer should be smoothened with fine glass paper and dust removed.
J.Byrne 2016

## Slide 4: Q 3.
Describe briefly how to apply a water based dye.
Water based dyes are available in a wide range of pigments. Pigments can be mixed with water or bought premixed. Timber surface will need to be dampened allowed to dry and sanded before the water based dye is applied because the water lifts the grain.
J.Byrne 2016

## Slide 5: Q 4.
Explain why surface finishes are applied to wood?
To protect the wood from oil, grease, liquids and other general pollution by sealing the pores. A finish will also enhance the natural beauty of the wood.
J.Byrne 2016

## Slide 6: Q 5.
Give three general Health & Safety precautions that should be observed when spraying lacquer.
Wear proper respiratory mask to protect your eyes, nose and mouth.
Spray in a well ventilated room.
Always check pressure valves and clocks when you first turn on the compressor.
J.Byrne 2016

## Slide 7: Q 6.
Name the 4 different groups of stains / dyes.
Water based stains/ Chemical stains.
Spirit based stains.
Oil based stains.
Solvent based stains.
J.Byrne 2016

## Slide 8: Q 7.
Explain briefly how a chemical stain works and is applied.
Chemical stains are made by mixing chemical crystals with water. These chemicals react with the tannic acid that is present in woods and thus change the colour.
As they are water based the grain will need to be pre- dampened and sanded before staining.
J.Byrne 2016

## Slide 9: Q 8.
What is the chemical stain Bichromate of potash. Explain briefly how this chemical stain works and is applied.
Chemical stains are made by mixing chemical crystals with water. These chemicals react with the tannic acid that is present in woods and thus change the colour.
Bichromate of potash will turn mahogany a darker brown each time it is applied to the surface so care is needed limit overlapping when applying.
J.Byrne 2016

## Slide 10: Q 9.
Suggest a suitable finish for each of the following, and give one reason for each choice:
A solid walnut kitchen worktop
Wardrobe doors
A solid oak floor
J.Byrne 2016

## Slide 11: Q 9.
A solid walnut kitchen worktop : Oil polish because it does not crack or blister or show heat or water.
Wardrobe doors: Nitrocellulose because it is cheap, quick drying and produces a hard heat and moisture proof finish.
A solid oak floor: Polyurethane because it has an excellent hard surface. Good heat, moisture and wear resistant properties. As water based product often used as a floor sealer, leaves no brush marks, excellent resistance to wear and tear.
J.Byrne 2016

## Slide 12: Q 10.
In relation to surface finishes:
a) What finish consists of a mixture of shellac in methylated spirits?
b) What type of finish should be used on a salad bowl ?
c) What does the term “de nib “ mean ?.
d) When spraying lacquer you sometimes get blooming, what is blooming?
J.Byrne 2016

## Slide 13: Q 10.
a) French polish.
b) A non toxic finish like bees wax, olive oil etc.
c) The term ‘de nib’ is the fine sanding between coats of polish or lacquer.
d) If conditions are too damp and cold the lacquer gets a white clouded film on its surface that has to be sanded off before applying the next coat.
J.Byrne 2016